# A Slightly Improved Printer Protocol

Bob Cousins
13 July 2012
## Current Method

The host sends Gcode command lines to the printer. The printer will either queue the command (a buffered command) or process it immediately (an unbuffered). In either case each command normally results in an “OK” response. When the print queue is full, the printer implements flow control by not sending an “OK”. When a new slot becomes available, the printer sends “OK”, and usually the host immediately sends another Gcode command.

So the host is sending data to the printer as fast as the printer can accept it, which is good.

## The Problem

The problem is that when the printer is busy, and the queue has filled, the host can no longer send any command, because it is waiting for an “OK”. There are some unbuffered commands which could still be processed like Get Temperatures or Motors Off. But the printer can't send an OK, because it doesn't know if the next command will be buffered or not. If the next command is a buffered command and the queue is still full, all it can do is reject it with RS response, but the host will sit in a busy loop trying to resend the exact same command.

## The Solution

The solution is to allow the host to send a command even when the queue is full. If the printer cannot process a buffered command, it will reply “BUSY”. Then the host must wait a bit before resending the buffered command. In the meantime, it can send any unbuffered command.

How does the host know if a command is buffered or not? In a way it doesn't need to – the printer will tell it. A command with a response should be held in a queue. The host can “interject” any other command, like Get Temperature which might be generated on timer tick, or if the user presses “Stop” on the host control panel, the host can try sending the command.

If it gets a BUSY response for the “interjected” command, it could ignore and try later, like a Get Temperature” poll. If it is an important command, it could be put at the top of a “retry later” queue. If it is less important but still useful, the host can do a round-robin on its send queue, and try commands until they are accepted.

The host could have a list of all known commands and their type, but this is less flexible, and would need constant maintenance, if indeed a comprehensive list of commands could be created.
## Setting Up
At start up, the host should query the firmware capabilities with M115. If the printer has the “busy” option, it will add BUSY_OPT:Y to the list. If the option is present, then the host should send the “M??? P1” command to turn on the option in the printer. Or the host just sends the request and gets OK or an error (“bad Mcode”)
If the option is turned on successfully, then the host can expect to get a BUSY.

## History

v1	13 July 2012 RMC First draft